# BLU code – procedure 3.3 - information terminal –ship

To the Master

Dear sir,

In accordance with the above mentioned code, please find hereunder the port/terminal information of the Kalootharbour Flushing

- General berth information

  - Name of berth:

- Berthingposition/Quay:

  - Berth available:

  - Commencement of (un)loading:

  - dischargingtime approx:

  - Normal workinghours Monday 06.00 hours till Saturday 06.00 hours.

- Loading/discharging equipment consists of : 3  floatingcranes (25 tons each) with pontoondimensions of 45 meters loa and 21 meters beam + 1 floating crane 36 tons (55 x 21 m)

  - Number of cranes available:

- Mooring alongside floatingcrane(s) and fenderpontoons. Vessel’s mooring lines on quay bollards according instructions of pilot/harbourauthorities but always enabling floatingcranes to reach all cargo in all holds.

- Information abt. minimum depth of water alongside the berth and in approach or departure channels will be supplied by pilot and/or harbourauthorities.

- Waterdensity at the berth is approx 		1.020

- Maximum distance between the waterline and top of cargo hatch covers or coamings is 19 meters.

No other airdraftlimitations.

- In view of distance between ship/shore, Stevedores will supply shore-gangway for safe access ship/shore.

  - Master is responsible to ascertain a continuous watch on tighteness of mooringlines.

  - It is strictly prohibited for vsls crew to leave the vessel/enter the terminal without verbal notice to the shift- supervisor. After such notice, the crewmember will be picked up by bus and transported to the terminaloffice.

  - Crewmembers leaving the terminal can only be picked up by taxi at the gangway.

  - It is prohibited for crewmembers to enter the holds while loading/ discharging and to move vesselscranes without notification the shift supervisor.

- Side of ship alongside the berth:

- Information about maximum allowed speed of approach to the berth and availability of tugs, type and bollard pull will be given by the pilot.

- Loading-/dischargingsequence: 		As per Master’s information

Terminal’s preferred option is for a two pass rotation over each hold, subject to complying with vessel’s stability and stress limitations. Holds will be discharged shovelclean. In case of discharging vessels which have inside structures such as cradles which are not easily accessible i.e. not fenced of stevedores will discharge grab clean.

- Cargo hazard : 				n/a

- Any changes in cargo handling operations or changing to existing plans will be passed on/discussed.

- Pontoondimension (beam) of floatingcranes is less than dimensions of  fenderpontoons resulting in a free movement of the cranes between ship/shore when shifting during the loading/dischargingoperation.

When changing the number of loading- unloading cranes (additional crane or crane leaving ship/shore) and assistance of crew is required, the Master will be contacted (with sufficient notice) by the terminal representative.

- Mooringlines required :			as per port regulations.

- Unusual mooring arrangements: 		No. Mooring-arrangement , see 3.

- Any restrictions on de-ballasting : 		as per port regulations.

- Maximum sailingdraft permitted by the port authority: as per port regulations.

- Other information required:

  - Type of hold-ladders and position. Information abt. any vulnerable parts in the holds (nozzles, fueltanks,pipes etc)

  - Please note that Stevedores reject liability for damage to australian ladders/railings/platforms inside the Holds, outside the frames.. Terminal is operating under Terms and Conditions Rotterdam Bulk Cargo Stevedores Rotterdam 1991. Details will be given upon arrival

- Any damages must be reported latest 4 hours after completion of cargo operations in that specific hold. Reporting of damages needs to be done in writing and handed to the Terminal Representative within this timeframe.

- OVET Terminals are ISPS compliant. Visitors to the ship are only allowed to enter the terminal after a  written notice from the SSO or the Agent to our PFSO. A crewlist must be provided by vsls officer to our PFSO. Other details of the procedure will be given upon arrival. Terminal in ISPS  fase 1